## Slide 1
Design Technology Information sheet Year 10 Plastics
This unit recaps polymers from last year. It also revisits ‘CAD’ in the form of Techsoft 2D and the use of the laser cutter ‘CAM’. The design process is covered and you will discover a range of design styles, ‘Bauhaus’ being the main focus.
Key words
Thermoplastics, thermosetting plastics, 6 R's.
Techsoft 2D, CAD, laser cutter CAM.
Bauhaus design, form follows function.
The polymer classifications and the differences between them. Understanding the properties and uses of some.
You will learn how past designers such as the Art Deco group were influenced and use this to develop their own designs.
The source of most polymers is ‘crude oil’. This is a finite resource that will run out. Use of polymers comes with a responsibility. The 6 R’s will be looked at during this project.
PET/PETE polyethylene terephthalate | Thermoplastic used for drinks bottles and packaging etc | 
PP Polypropylene | Thermoplastic Used for chairs, rugs,containers etc | 
UF Urea Formaldehyde | Thermosetting plastic Used for plug casings and sockets | 
MF Melamine formaldehyde | Thermosetting plastic Used for worktops and cooking utensils | 
The Bauhaus is a German artistic movement which lasted from 1919-1933. Its goal was to merge all artistic mediums into one unified approach, that of combining an individual's artistry with mass production and function. Bauhaus design is often abstract, angular, and geometric, with little ornamentation.
Health & Safety
Line Bender
Risk - Burning hands on the element.
Control - Wear heat proof gloves
Using Tensol
Risk - Getting chemicals on hands, breathing in fumes
Control - use a clamp and small brush to apply. Use in a well ventilated area.
CAD
CAD/CAM
Computer Aided Design
Computer Aided Manufacture
Advantages - More accurate than traditional hand drawn orthographic drawings. Faster to produce and less labour intensive. Multiple copies can be stored, printed and shared electronically. Can be easily edited and design modifications do not generate endless re-drawings of the original design.
Disadvantages - Work can be lost because of the sudden breakdown of computers.
Work is prone to viruses.
Work could be easily “hacked”
Time taking process to know how to operate or run the software.
CAM
Advantages - Greater speed in producing components.
Greater accuracy and consistency, with each component or finished product exactly the same.
Greater efficiency as computer controlled machines do not need to take breaks.
Disadvantages - Computer errors are possible.
CAD and CAM software can be expensive.
Training is expensive.
Computers and controllers to run the software and CNC machinery for manufacturing is expensive.